## Slide 1: Beam Instrumentations in J-PARC Linac
Akihiko Miura
Beam Monitor Gr., J-PARC

## Slide 2: Contents
Akihiko Miura, J-PARC
1. Introduction
  About J-PARC Linac & its Instrumentations
2. Topics of Beam Instrumentations
  Accelerator Tuning & Ordinal Observations of Operation
  Beam Profile Monitors (trans. and long. Profiles)
  Beam Loss Monitors
3. Summary

## Slide 3: 1. Introduction
Akihiko Miura, J-PARC
J-PARC Linac
Materials and Life Science
Experimental Facility
Hadron Beam Facility
５００ｍ
Linac
(400 MeV)
Neutrino to Kamiokande
(for T2K experiment)
J-PARC = Japan Proton Accelerator Research Complex
3 GeV Rapid Cycle Synchrotron (RCS)
30 GeV Main Ring (MR)
Pacific Ocean

## Slide 4: 1. Introduction
Akihiko Miura, J-PARC
Parameters of J-PARC Linac
Ion species: Negative hydrogen ion
RF frequency: 324 MHz (972 MHz for ACS cavities)
Output energy: 400 MeV
Peak current: 50 mA, (60 mA trial already completed)
Pulse width: 0.5 msec
Repetition rate: 25 Hz
Chopper beam-on ratio: 54% (MLF) / 56% (MR)
Beam power: 135 kW (MLF) / 140 kW (MR)
IS
RFQ
DTL
SDTL
ACS since 2012
MEBT1
MEBT2
L3BT
50keV
3MeV
50MeV
191MeV
400MeV
Transverse
halo scrapers
L3BT
1st arc
L3BT 2nd arc
RCS injection
Debuncher
Cavity

## Slide 5: 1. Introduction
Akihiko Miura, J-PARC
Operation History
Year | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
I [mA] | 5 | 5 ~ 15 | 15 | 15 | 15 | 15 | 15 ~ 30 | 30 | 30 ~ 40 | 40 | 40 ~ 50 | 50 | 50
P [kW] | - | ~ 100 | 100 ~ 200 | 100 | 200 ~ 300 | 300 | 300 ~ 400 | 500 | 150 ~ 200 | 150~ 400 | 400 ~ 500 | 500 | 500
Tohoku
Earthquake
Hadron
Facility
Accident
MLF Target Failure
Event of
Beam
Interruption
I: Peak Beam Current
P: Output at 3-GeV exit
Energy Upgrade
from 181 to
400 MeV
Longitudinal Position [m]
0
100
200
300
400
40mm
20mm
Vertical Deformation [mm]
0
10
-20
-40
-10
-30
-50
Damage on Accelerator Tunnel
ACS Accelerator Cavities
K. Hasegawa, et. al., JPS Conf. Proc. , 011012 (2015)

## Slide 6: Contents
Akihiko Miura, J-PARC
1. Introduction
  About J-PARC Linac & its Instrumentations
2. Topics of Beam Instrumentations
  Accelerator Tuning & Ordinal Observations of Operation
  Beam Profile Monitors (trans. and long. Profiles)
  Beam Loss Monitors
3. Summary

## Slide 7: 2. Topics of Beam Instrumentations
Akihiko Miura, J-PARC
Accelerator Tuning & Ordinal Observations of Operation
BPM (Beam Position Monitor)
beam orbit correction
Beam Current Monitor (Slow CT)
cavity transmission optimization
Beam Phase Monitor (Fast CT)
amplitude and phase setting of cavity
Trans. Profile Monitor (Wire Scanner)
optics of beam transfer (settings of quadrupoles)
Acceleration Cavity
Acceleration Cavity
FCT/SCT
FCT/SCT
BPM
WS
Quadrupole Magnet
Beam line
BPM
Strip-line type BPM
Resolution
Δx<~0.1 mm
Δy<~0.1 mm
Fast & Slow current transformer for the beam phase & current monitor.
Dynamic Range
SCT: 0.1 – 80 mA
FCT: > 30dB
Winding coil,
SCT: Fifty turns
FCT: Single turn
Resolution,
SCT: ΔIbeam < 1.0 %,
Imin ~ 0.1 mA
FCT: Δφbeam < 1.0 deg.
Energy: < 0.1 %
A. Miura, et. al., IOP Conf. Series: Journal of Physics: Conf. Series 874 (2017) 012080

## Slide 8: 2. Topics of Beam Instrumentations
Akihiko Miura, J-PARC
Earthquake attack (Vacuum leakage)
Brazing section between the ceramic tube and stainless duct was broken.
Corroded pre-amplifier boxes on the floor by strong alkaline.
Great earthquake occurred on March 11, 2011.
The seismic intensity: 6-minus (JMA scale)
Because the tsunami-height was fortunately below the floor level of J-PARC, alkali water leakage occurred from cracks of concrete wall.
Accelerator Tuning & Ordinal Observations of Operation
A. Miura, et. al., WEPC144, Proceedings of IPAC2011, San Sebastián, Spain

## Slide 9: 2. Topics of Beam Instrumentations
Akihiko Miura, J-PARC
Transverse Profile Monitor, “Wire Scanner”
Motor Unit
45 deg.
Tungsten
Wire
Carbon Plate for
Vertical Beam Size
Ceramic Frame
Resolution
σx < 0.1 mm
σy < 0.1 mm
Horizontal Profile
SDTL03A
Range
halo
200 mV/div, 40 us/div
Signal Obtained at the Peak of Beam Pulse
Pulse Height
Beam Profile Monitors (trans. and long. Profiles)
A. Miura, et. al., Journal of the Korean Physical Society, Vol. 69, No. 6, September 2016, pp. 1005

## Slide 10: 2. Topics of Beam Instrumentations
Akihiko Miura, J-PARC
Transverse Profile Monitor, “Wire Scanner”
Beam Profile Monitors (trans. and long. Profiles)
Application of carbon nanotube wire
A. Miura, et. al., IOP Conf. Series: Journal of Physics: Conf. Series 1067 (2018) 072020
Waveform of Signal from CNT Wire at 100 μs operation.
Beam profile taken by CNT wire and carbon fiber

## Slide 11: 2. Topics of Beam Instrumentations
Akihiko Miura, J-PARC
Transverse Profile Monitor, “Wire Scanner”
Beam Profile Monitors (trans. and long. Profiles)
Application of carbon nanotube wire
A. Miura, et. al., IOP Conf. Series: Journal of Physics: Conf. Series 1067 (2018) 072020
Wire Damage
Direct observation by microscope (x50)

## Slide 12: 2. Topics of Beam Instrumentations
Akihiko Miura, J-PARC
Longitudinal Profile Monitor, “Bunch Shape Monitor”
Beam Profile Monitors (trans. and long. Profiles)
Amplitude tuning using scan curve and Twiss parameters is trying.
s2BSM= ez[(1+Lk)2bB-2L(1+Lk)aB+L2gB]
ez is emittance,
L is drift length,
aB, bB, gB are Twiss parameter,
k is longitudinal focusing force.
Bunch shape monitor installed at beginning of ACS section
Optimization of buncher settings based on the amplitude scan.
IOP Conf. Series: Journal of Physics: Conf. Series 874 (2017) 012080
Amplitude Scan by Buncher 1

## Slide 13: 2. Topics of Beam Instrumentations
Akihiko Miura, J-PARC
Investigation on RF-abnormarity
Detection of the RF-feed forward/back failure utilized by bunch shape monitor
Unsatisfied beam-loading compensation can be found in deformed pulse shape.
Consistency can be obtained by FCT.
Adjustment of the RF-feed forward power
Failure of the RF-feed forward power
(example: failure at DTL1, 2 and 3)
FF region
Waveform taken by FCT located at downstream of BSM
Beam Profile Monitors (trans. and long. Profiles)

## Slide 14: 2. Topics of Beam Instrumentations
Akihiko Miura, J-PARC
Beam Loss Monitor (BLM)
Gas Proportional Counter
Beam line
SDTL Cavity
Quadrupole Magnet
Scintillation Monitor
Gas Proportional BLM, E6876 - 600
Toshiba Electron Tubes & Devices Co. Ltd.,
Anode Pt Wire, Φ50um (Gas: Ar+CO2)
Sensitive for charged particle, X-ray and gamma-ray
Time response
t < 1.0 ms
Length: 600mm
Diameter: 50.8 mm
Gas pressure: 1 atm
Beam Loss Monitors

## Slide 15: 2. Topics of Beam Instrumentations
Akihiko Miura, J-PARC
Beam Loss Monitor (BLM), Scintillation Beam Loss Monitor
Accelerator Tuning & Ordinal Observations of Operation
600us
Yellow: S15_SCT01
Pink: S13B_Scintillator
Green: S13B_BLM
160ns
160ns
600ns
40ns
Gas proportional BLM is sensitive to X-ray from the cavity.
Proportional
Scintillator
Beam (CT)
Photo-multiplier: Hamamatsu H3164-10
(gain : 1.1 x 106, peak wavelength : 420 nm)
Plastic scintillator: Saint-Gobain BC-408
(peak emission wavelength: 425 nm)
Less X-ray sensitivity
Clear beam loss signals with low noise
High time resolution
A. Miura, et. al., MOPD43, Proceedings of DIPAC2011, Hamburg, Germany

## Slide 16: Summary
Akihiko Miura, J-PARC
1. Introduction
  About J-PARC Linac & its Instrumentations
  Parameters of J-PARC Linac
  Operation History
2. Topics of Beam Instrumentations
  Accelerator Tuning & Ordinal Observations of Operation
  Earthquake attack (Vacuum leakage)
  Beam Profile Monitors (trans. and long. Profiles)
  Transverse Profile Monitor; Wire Scanner
  Longitudinal Profile Monitor, “Bunch Shape Monitor”
  Beam Loss Monitors
  Gas Proportional Counters
  Scintillation Beam Loss Monitor
3. Summary

## Slide 17
Akihiko Miura, J-PARC
Thank You