## Slide 1: Warm and cold SNS LINAC commissioning
A. Aleksandrov
Spallation Neutron Source,
Oak Ridge National Laboratory, TN USA
Warm and cold SNS LINAC commissioning

## Slide 2: SNS Accelerator Complex
H- stripped to protons
Current
1ms
Front-End: Produce a 1-msec long, chopped, low-energy H- beam
LINAC: Accelerate the beam to 1 GeV
Accumulator Ring: Compress 1 msec long pulse to 700 nsec
Deliver beam to Target
Ion Source
2.5 MeV
1000 MeV
86.8 MeV
CCL
SRF, b=0.61
SRF, b=0.81
186 MeV
387 MeV
DTL
RFQ
P beam on target : 1.44MW
I beam average: 1.44mA
Maximum Beam energy: 1 GeV
Duty factor: 6%
Rep. rate: 60Hz
Pulse width: 1ms

## Slide 3
2.4845 ns (1/402.5 MHz)
260 micro-pulses
645 ns
300 ns
945 ns (1/1.059 MHz)
1ms
16.7ms (1/60 Hz)
15.7ms
Macro-pulse
Structure (made by the Ion Source)
Mini-pulse
Structure (made by the choppers)
Micro-pulse
structure
(made by the RFQ)
SNS beam pulse temporal structure

## Slide 4: SNS commissioning timeline

## Slide 5: SNS power ramp up and operation timeline
PPU,2MW
STS, 2.8MW
~ (3 + 1) years to ramp to nominal 1.4MW power

## Slide 6: 2.5MeV 402.5MHZ RFQ
Initial commissioning at Berkeley
  Half of full power beam test
  Output beam current (‘’transmission’’)
  Transverse beam emittance
Re-commissioning at SNS
  Beam energy (Time-of-Flight)
  Full power beam test
No surprises encountered
Output current vs. RF amplitude
Vertical beam emittance
Raw signal from two BPMs

## Slide 7: Testing new RFQs at SNS Beam Test Facility
Beam Transmission
Beam Energy
Beam emittances (Kiersten Ruisard’s talk on Thursday)
  6-dimensional or any projection
Beam halo
  High Dynamic Range (106) 2-dimensional scan
RF amplitude x-ray calibration
Full beam power test
Proton contamination fraction
y [mm]
y’ [radian]
Movable phase detector (BPM)
phase
energy
position
phase

## Slide 8: What we learned about SNS RFQ
Very robust machines, capable to take some abuse
RF amplitude acceptable range is much larger than expected
Transmission is major figure of merit
SNS linac does not require significant tuning when changing RFQ amplitude in wide range
~65%
~85%
100%
~83%
Transmission
RF filed

## Slide 9: 2.5MeV SNS MEBT (fast chopper beamline)

## Slide 10: MEBT in-line diagnostics
 | Measured parameter | quantity | Use for commissioning | Use for machine tuning | Use in operation | Use in Beam study
Beam Loss Monitor (BLM) | radiation Ionizing, n | 2 | Yes | No | No | No
Beam Current Monitor (BCM) | beam current | 2 | Yes | Yes | Yes | Yes
Beam Position Monitor (BPM) | x, y, z position | 6 | Yes | Yes | No | Yes
Wire scanner (WS) | x, y 1-d profile | 5 | Yes | No | No | Yes
Differential BCM | In-out beam current | 1 | No | No | Yes | No
Emittance Scanner | x, y 2-d emittance | 1 | Yes | No | No | Yes
Chopper monitor (ChoMPS) | Fast, HDR beam current | 1 | No | No | Yes | No
Laser Wire | longitudinal 1-d profile | 1 | Yes | No | No | No*
X
added later
eliminated

## Slide 11: What we learned about SNS MEBT
Can operate without fast chopper
  Chopper was removed
Linac operation is not very sensitive to MEBT optics
Measure transverse profiles using 5 wire scanners
Search for input Twiss parameters to best fit model to measured data
Repeat several times with different quad settings
horizontal
vertical

## Slide 12: 86.7 MeV 402.5MeV Drift Tube Linac (DTL)
2.5 MeV
Tank 1
Tank 2
Tank 3
Tank 4
Tank 5
86 MeV
36.57 meters
Tank 6
Six tanks accelerate beam to 87 MeV
System includes 210 drift tubes, transverse focusing via PM quads, 24 e/m dipole correctors, and beam diagnostics
12 well-defined set points to establish: 6 RF amplitudes, and 6 RF phases

## Slide 13: DTL Tank 1 was commissioned using temporary “D-plate”
Bunch Shape Monitor
(BSM)
No surprises encountered

## Slide 14: DTL in-line diagnostics
 | Measured parameter | quantity | Use for commissioning | Use for machine tuning | Use in operation | Use in Beam study
Beam Loss Monitor (BLM) | radiation Ionizing, n | 11+12 | Yes | Yes | Yes | Yes
Beam Current Monitor (BCM) | beam current | 6 | Yes | No | No | No
Beam Position Monitor (BPM) | x, y, z position | 10 | Yes | Yes | No | Yes
Wire scanner (WS) | x, y 1-d profile | 6 | Yes | No | No | Yes
Differential BCM (DBCM) | In-out beam current | 1 | No | No | No | No
Faraday Cup with energy degrader (FC) | beam current above energy cutoff | 6 | Yes | Yes | No | Yes

## Slide 15: What we learned about DTL
The RF amplitude acceptable range is larger than expected
Is DTL a collimator?

## Slide 16: 187MeV 805 MHz Coupled-Cavity Linac (CCL)
48 accelerating segments,
48 quadrupoles, 8+8 independent power supplies, 40 trims
32 steering magnets and diagnostics
8 well-defined RF set points to establish: 4 RF amplitudes, and 4 RF phases
16 loosely-defined set points for quadrupoles power supplies

## Slide 17: CCL baseline diagnostics
 | Measured parameter | quantity | Use for commissioning | Use for machine tuning | Use in operation | Use in Beam study
Beam Loss Monitor (BLM) | radiation Ionizing, n | 48* + 10 | Yes | Yes | Yes | Yes
Beam Current Monitor (BCM) | beam current | 2 | Yes | No | No | No
Beam Position Monitor (BPM) | x, y, z position | 10 | Yes | Yes | No | Yes
Wire scanner (WS) | x, y 1-d profile | 8 | Yes | No | No | Yes
Beam Shape Monitor (BSM) | longitudinal 1-d profile | 3 + 1 | Yes | No | No | Yes*
eliminated
X

## Slide 18: What we learned about SNS CCL
The RF amplitude acceptable range is larger than expected
The transverse optics is more flexible than expected
There is significant flux of field emitted electrons coming out
Transverse alignment of RF cavities is questionable

## Slide 19: 1GeV 805 MHz Superconducting Linac (SCL)
23 cryomodules with 81 SC cavities operating at 2.1K
32 Doublets of quadrupole magnets and diagnostics in warm sections between cryo-modules
Medium beta cavity
High beta cavity
162 loosely-defined RF set points to establish: 81 RF amplitudes, and 81 RF phases
32 loosely-defined set points for magnets power supplies

## Slide 20: SCL baseline diagnostics
 | Measured parameter | quantity | Use for commissioning | Use for machine tuning | Use in operation | Use in Beam study
Beam Loss Monitor (BLM) | radiation Ionizing, n | 76 + 23 | Yes | Yes | Yes | Yes
Beam Position Monitor (BPM) | x, y, z position | 32 | Yes | Yes | No | Yes
Laser Wire (LW) | x, y 1-d profile | 9 | Yes | No | No | Yes
Laser Emittance Scanner (LES) | x,y 2-d emittance; longitudinal 1-d profile | 1 | No* | No | No | Yes
added later

## Slide 21: What we learned about SNS SCL
Intra-beam stripping is significant source of beam loss
  Major discovery during commissioning
  All beam diagnostics were important for discovery
Very flexible tuning parameters
  Large flexibility of synchronous phase profile
  Can operate with missing RF cavities or even cryomodules
  Empirical tuning of transverse beam dynamics
Use reduced charge beam pulse for tuning
  <1us, <1mA
No clear relation between RMS parameters and beam loss
  Output RMS emittance ~3 times larger than design value when tuned for minimum beam loss

## Slide 22: Diagnostics performance during commissioning
In general, performance was better than documented requirements
  BPM design minimum beam current and pulse width were 6mA, 5us. Works well with <1mA, <1us pulse
  Wire Scanner design dynamic range was <100. Achieve >10,000 with software modification and diagonal wire removal
Possible improvements
  Add gain control for BPMs
  Use 402.5MHz operating frequency instead of 805MHz (or both) for MEBT BPMs
  Reduce laser beam reflections in SCL laser wire
  Increase BSM resolution to ~1ps

## Slide 23: What’s for the future?
Can we control beam loss based on knowledge rather than empirically?
  Beam distribution measurements with dynamic range relevant for beam loss, e.g., up to 1ppm (halo)
  Bunch characterization in 6-dimensional phase-space
  Tools and techniques for model vs. real machine benchmarking
  ???

## Slide 24: Summary
SNS linac was successfully commissioned for design power operation in ~6 years
Baseline diagnostics were, in general, sufficient for all commissioning stages
SNS linac design is robust with larger tuning margins than anticipated
Beam Position and Phase Monitors are major tool for linac tuning
Beam Loss Monitors are major tool for empirical loss minimization at high power
We did not find good ways of using measured RMS beam parameters for linac tuning or operation
Motivation and direction for future SNS diagnostics development is to enable knowledge-based loss control