## Slide 1
Speaker: A. Sánchez-Caballero
A. Sánchez-Caballero, V. Alcayne, D. Cano-Ott, E. Mendoza, A. Pérez de Rada
CIEMAT– Unidad de Innovación Nuclear
Deep Learning applied to Capture Cross Section Data Analysis
Taller aplicaciones IA para proyectos CIEMAT

## Slide 2
DL and nuclear data: neutron capture classification
Problem definition
The Total Absorption Calorimeter (TAC) at nTOF provides the deposited energy of gamma rays in 40 BaF2 crystals. For each registered event, we have the number of activated crystals (mcr) and the sum of the deposited energy (Esum).
neutron

## Slide 3
DL and nuclear data: neutron capture classification
Problem definition
The Total Absorption Calorimeter (TAC) at nTOF provides the deposited energy of gamma rays in 40 BaF2 crystals. For each registered event, we have the number of activated crystals (mcr) and the sum of the deposited energy (Esum).
Nuclear reaction

## Slide 4
DL and nuclear data: neutron capture classification
Problem definition
The Total Absorption Calorimeter (TAC) at nTOF provides the deposited energy of gamma rays in 40 BaF2 crystals. For each registered event, we have the number of activated crystals (mcr) and the sum of the deposited energy (Esum).
Absorbed γ-rays

## Slide 5
DL and nuclear data: neutron capture classification
Problem definition
Current method: specific cuts or constraints on Esum and mcr values of each event to improve the signal-to-background ratio.
For 197Au(n,γ):
Objective: to build a DL model for classification of capture/non-capture events from TAC signals and compare with current method.
Deposited energy distribution of the 197Au(n,γ) measurement under different constraints in crystal multiplicity.
Image source: Carlos G. Guerrero Ph.D. thesis “Measurements of the 237Np and 240Pu neutron capture cross sections at the CERN nTOF facility” (2008)
mcr>2
2.5<Esum<7 MeV

## Slide 6
Deep Learning
Deep Learning models have proved to be good classifiers of text, audio, image, and video samples.
In our case, we have high dimensionality data (40 signals from the TAC crystals) and we can generate a big dataset with Monte Carlo simulations. Appropriate conditions to try neural networks as discriminator of capture events.
DL and nuclear data: neutron capture classification

## Slide 7
DL and nuclear data: neutron capture classification
Methodology
Input: 40-sized arrays of deposited energy in each crystal from Monte Carlo simulations of a 197Au measurement experiment.
Neural Network classifier: a model with 5 dense layers, 18K trainable parameters, binary cross-entropy loss function, and Adam optimizer, using the Keras API for Python. The NN classifies between capture (0) and non-capture (1).
Edep,1
Edep,2
Edep,40
Neural Network
Prediction
{0…1}
Neutron source
n (10-2 – 105 eV)
197Au sample
100 µm width
Ø 2.0 cm
1 cm
Ø 2.5 cm
TAC@nTOF
Capsule of Al,

## Slide 8
DL and nuclear data: neutron capture classification
Methodology. Network architecture
Combinations of DL with different cuts on Esum and mcr are studied.
The performance of all methods are evaluated through the values of:
  εγ,rel = capture detection efficiency. Set to 1 for the dataset without any cut.
  Ri = signal-to-background ratio in the i-th interval of the incident neutron energy spectrum. Calculated as true capture events divided by non-capture events.
BN+LR = Batch Normalization + Leaky ReLU activation
200
neurons
100
100
50
1
y=0
y=1
BN+LR
BN+LR
BN+LR
BN+LR
Input
layer
Dense
(or Fully Connected)
Dense
Dense
Dense
Dense
Sigmoid activation

## Slide 9
Results and comparison with traditional method
Applying more precise and relaxed cuts allow us to obtain similar results but also with higher relative capture efficiency.
Capture efficiencies, εγ,rel :
Std. cuts = 55%
Std. cuts + DL = 43%
New cuts + DL = 62%
Scaled down
X0.01
Scaled up
X10
197Au with aluminum canning

## Slide 10
Results and comparison with traditional method
Case of a fissile sample: 239Pu
Example of using traditional cuts with or without DL for data including fission events.
Figure shows the full-spectrum capture-to-background ratio.
Capture-to-fission rate in original data (no cuts): ~0.5
Some capture efficiencies, εγ,rel :
2.5<Esum<7;2<mcr<6 = 73%
Std. cuts + DL = 63%
Esum>2.5;mcr>1 + DL= 77%
*
(*): ratios calculated adding the Esum<7 MeV constraint to the indicated cut (X axis).

## Slide 11
Results and comparison with traditional method
Deposited energy spectrum: 197Au simulation
With Deep Learning
Without Deep Learning
For neutron energies between 1 keV and 2 keV

## Slide 12
Results and comparison with traditional method
Deposited energy spectrum: 239Pu simulation
With Deep Learning
Without Deep Learning

## Slide 13
Additional results
Simulating a faulty detector in the TAC
We set Edep of Detector#1 to a fixed value of 0.001 MeV for all events.

## Slide 14
Additional results
Simulating a faulty detector in the TAC
We set Edep of Detector#1 to a fixed value of 0.001 MeV for all events.
The algorithm successfully identifies the defective crystal.