## Slide 1
Development of a new large gas cell with electric field guidance for IGISOL (Task 1.1.2.)
Heikki Penttilä [& IGISOL group]
University of Jyväskylä, Accelerator laboratory

## Slide 2: Development of a new large gas cell with electric field guidance for IGISOL
What has been done:
The capability of the means of faster ion extraction studied utilising simulations
The site specific constraint at IGISOL (space, radiation, high voltage) surveyed
Suitable means for IGISOL adopted
Detailed technical drawings will be produced
D.1.2 “Report on the design of the large gas cell for IGISOL”, due M24 – delayed, delivered 1.11.2023, M51
Gao, Z., et al., (2023). "New design and simulation of the ion guide for neutron-induced fission products at the IGISOL facility", proceedings of the 15th International Conference on Nuclear Data for Science and Technology (ND2022), 21-29 July 2022, online. EPJ Web of Conferences, 284, Article ID 04011.
Description of the work:
The JYU will improve the quality of the neutron induced fission product collection at IGISOL by the design of a new gas cell with electric field guidance. This new device will allow better efficiency which is expected to be of the order of 100 compared to what exist today. This improvement will benefit greatly for the fission products studies.

## Slide 3: Development of a new large gas cell with electric field guidance for IGISOL
In the ion guide technique, reaction products are stopped in helium as ions and transported as ions to further analysis.
Target
SPIG electrode
Beam
Extractor
Possible solution: large stopping gas cell with electric field guidance
At the IGISOL the ions are transported with the gas flow alone. This limits the size of gas cell: bigger gas cell is not better, since the ion survival time is limited.
Stopping efficiency for the fission products in the current fission ion guide is ≈ 0.75 %, and their mean extraction time is ≈ 100 ms.
  Needed:
  higher stopping efficiency
  faster extraction.
NIMA 770 (2015) 87
GSI cryogenic gas cell
NIMB 463 (2020) 378
ACGS (Advanced Cryogenic Gas Stopper) at NSCL
ANL CARIBU
NIMB 376, (2016) 246

## Slide 4: Development of a new large gas cell with electric field guidance for IGISOL
Cryogenity? …eventually, no.
  Benefit:
  higher gas density, so better stopping efficiency
  Freesing of impurities
  Operation of RF carpets easier in lower pressure
  Challenge:
  Technically complicated, space consuming
  Combining with neutron production target (heat and cryo dont mix well)
  Denser space charge
  It is not only stopping, extraction matters as well:
  Ion mobility while density so extraction time
NIMB 397, (2016) 1

## Slide 5: Development of a new large gas cell with electric field guidance for IGISOL
EPJ Web of Conferences 284 (2023) 04011
Electric field simulations:
25 by 30-40 cm cylinder ring electrodes to generate DC field;
RF-carpet on the end of the cylinder; RF-field about 6 MHz; 10 concentrig rings to enhance the electric field towards the exit nozzle
here n-induced fission similar as performed with modified current fission ion guide (see below).

## Slide 6
SPIG
CURRENT GAS CELL
NEW GAS CELL
EXTRACTOR
EXTRACTOR
SPIG
Development of a new large gas cell with electric field guidance for IGISOL
Proton induced fission

## Slide 7
BEAM
Development of a new large gas cell with electric field guidance for IGISOL

## Slide 8
What has been done:
The capability of the means of faster ion extraction studied utilising simulations
The site specific constraint at IGISOL (space, radiation, high voltage) surveyed
Suitable means for IGISOL adopted
Detailed technical drawings will be produced
D.1.2 “Report on the design of the large gas cell for IGISOL”, due M24 – delayed, delivered 1.11.2023, M51
Gao, Z., et al., (2023). "New design and simulation of the ion guide for neutron-induced fission products at the IGISOL facility", proceedings of the 15th International Conference on Nuclear Data for Science and Technology (ND2022), 21-29 July 2022, online. EPJ Web of Conferences, 284, Article ID 04011.
Development of a new large gas cell with electric field guidance for IGISOL