## Slide 1: Design and Implementation of 3 Dimensional Data Visualization in Virtual Tokamak
1D. Li, 1,2B. J. Xiao, 1Q. P. Yuan, 1D. L. Chen, 1M.N. Jia
1Institute of Plasma Physics, Chinese Academy of Sciences, China
2Center of Hefei physical science and technology, University of Science and Technology of China, Hefei, China.

## Slide 2: OUTLINE
Motivation
  Integration the visualization of data with EAST model
  The procedure for the visualization of EAST
  The previous work about virtual EAST
Virtual Tokamak System
  Platform architecture
  Underlying framework
  Data Visualization in Virtual Tokamak
  Magnetic field visualization
  2D magnetic field
  Poincare plot of 3D magnetic field perturbations
  Summary
Notes: I will introduce my work from 4 parts. Firstly, I will discuss the motivation.

## Slide 3: Integration the visualization of data with EAST model
EAST design and engineering models
Detailed diagnosis information
Simulation and analysis results
Detailed magnetic measurement information
EAST model visualization
Data visualization
Database
MySQL
MDSplus
Rendering time<5s
Framerate>40FPS
Virtual Tokamak
  In order to realize fusion energy, we need to resolve many scientific and engineering challenges.
  The operation and maintenance of fusion device in the limited space are also a critical subject.

## Slide 4: The procedure for the visualization of EAST
Original CAD Data
fbx Format
Retopology
Rendering
  The EAST tokamak is chosen as the target device in this development.
  EAST consists of numerous components. It is upgraded every few years.
  Catia is used to design and create the EAST model.The sizes of the catia data are about 3GB.
  Unreal Engine 5 is chosen as the main development tool to render the EAST model and visualize the relevant data.
  The detailed Catia data is not suitable for the game engine. It is essential to convert the highmesh data into low polymesh forms.
  3dsMax is used to simplify and optimize the model.

## Slide 5: The previous work about virtual EAST
Data visualization
EAST host model
EAST vacuum model reconstruction
Window map
Magnetic probe virtual installation
Installation in realistic scene
  In the previous work, EAST model visualization has been realized for diagnosis components virtual installation. Particle trajectory data has been realized in the EAST.
  EAST divertor has been upgraded in recent years. The performance of virtual EAST has been improved. More comprehensive data visualization has also been attempted to be incorporated into the system.

## Slide 6: OUTLINE
Motivation
  Integration the visualization of data with EAST model
  The procedure for the visualization of EAST
  The previous work about virtual EAST
Virtual Tokamak System
  Platform architecture
  Underlying framework
  Data Visualization in Virtual Tokamak
  Magnetic field visualization
  2D magnetic field
  Poincare plot of 3D magnetic field perturbations
  Summary
Notes: I will introduce my work from 4 parts. Firstly, I will discuss the motivation.

## Slide 7: Platform architecture
  According to system requirements, some model files like CAD or Catia files and EAST photos are collected.
  In order to visualize 3D data, Machines data, experiment data and diagnostic data are read or exported from database.
  Unreal Engine 5 is chosen to realize the system. In the system, 3D EAST roaming and components visualization are implemented.
  Three kinds of data are visualized.
  In the Server, Data storage and optimization are realized. Data can be read from MDSplus.
  In the Client, components can be chosen to display or hide in the tree list.
Notes: According to system requirements, some model files like CAD or Catia files and EAST photos are collected. In order to visualize 3D data, Machines data, experiment data and diagnostic data are read or exported from database. Unreal Engine 5 is chosen to realize the system. In the system, 3D EAST roaming and components visualization are implemented. Three kinds of data are visualized. In the Server, Data storage and optimization are realized. Data can be read from MDSplus. in the Client, Components can be chosen to display or hiden in the tree list.

## Slide 8: Underlying framework
  Real time and history datase are deployed to store relevant data.
  In Java backend, real time data is subscribed and then analyzed and encapsulated to JSON.
  WebSocket service is established to send subscription request.
  In history processing logic, we can analyze or down sample or encapsulate data to json, query history data from history database.
  In front-end VUE, component echarts are renderered from realtime data process and history data process.
Notes: Three kinds of data type are visualized in the system, real time data, Mdsplus storage data and simulation data.

## Slide 9: Virtual EAST
Notes: EAST model is re-established, optimized and rendered in Unreal Engine 5.
Two tree lists are designed to display or hide relevant components and data visualization.

## Slide 10: OUTLINE
Motivation
  Integration the visualization of data with EAST model
  The procedure for the visualization of EAST
  The previous work about virtual EAST
Virtual Tokamak System
  Platform architecture
  Underlying framework
  Data Visualization in Virtual Tokamak
  Magnetic field visualization
  2D magnetic field
  Poincare plot of 3D magnetic field perturbations
  Summary

## Slide 11: Magnetic Field Visualization
  The toroidal magnetic probe (two-dimensional structure, 38 sets in the toroidal direction) is used to measure the internal magnetic field of the vacuum vessel, primarily for plasma shape inversion and equilibrium control.
  38 magnetic probes correspond to 38 signal names, and each signal can measure the magnetic field value at a certain moment.

## Slide 12
View the magnetic field in Webscope.

## Slide 13: 3D magnetic field visualization
In 2D space, 38 values are set to the 38 points.
Rotate the contour to render 3D magnetic field visualization.

## Slide 14: 2D Magnetic Field
  EFIT
  Solves the problems of plasma two-dimensional balance in tokamak
  GFILE
  Standard output file of the EFIT program
  Standard input file format of some other programs
  The number of grid points, flux value of calculation grid, plasma boundary location, plasma profile information
Read GFILE
Draw grid
Assign value
Draw contour
Draw line
Set angle
Set number
Render
result
grid lines
Assign magnetic flux value to grids
number of isolines
boundary magnetic flux
rotation angle
2D magnetic field visualization
Notes: The process of visualizing 2D magnetic field is figured. GFILE is read and grid lines are drawn. Then Magnetic flux value is assigned to grids, number of isolines is set to draw contour. Boundary magnetic flux and rotation angle are set and at last, 2d magnetic field visualization result is rendered.

## Slide 15: 2D Magnetic Field
Contour of Magnetic Flux
Data Visualization in Virtual EAST

## Slide 16: Poincare plot of 3D magnetic field perturbations
  Under ideal condition, the magnetic flux surface in tokamak is nested torus and toroidal axisymmetric.
  With the resonant magnetic perturabion (RMP) application, the 3D magnetic topology is changed and the magnetic field became toroidal asymmetry.
  1) The radial perturbed fields broke the rational surfaces to create island chains;
  2)the overlapped island chains in the edge creat a stochastic layer;
  3) the perturbed invariant manifolds of the separatrix creat homoclinic tangels around the X-point.
【M. Jia et al 2018 Nucl. Fusion 58 046015】
【M. Jia et al 2016 Plasma Phys. Control. Fusion, 58 055010】
Notes: The figure shows an example of combined geometry of the machine and the 3D magnetic topology, represented by a Poincare Plot on one toroidal position of the resonant magnetic perturbation application in EAST. The visulization of the 3D magnetic topology in the machine provide an intuitive background which can help researchers analyse other experimental observations.

## Slide 17: Poincare plot of 3D magnetic field perturbations
  The figure shows an example of combined geometry of the machine and the 3D magnetic topology, represented by a Poincare Plot on one toroidal position of the resonant magnetic perturbation application in EAST.
  The visulization of the 3D magnetic topology in the machine provide an intuitive background which can help researchers analyse other experimental observations.

## Slide 18: OUTLINE
Motivation
  Integration the visualization of data with EAST model
  The procedure for the visualization of EAST
  The previous work about virtual EAST
Virtual Tokamak System
  Platform architecture
  Underlying framework
  Data Visualization in Virtual Tokamak
  Magnetic field visualization
  2D magnetic field
  Poincare plot of 3D magnetic field perturbations
  Summary
Notes: I will introduce my work from 4 parts. Firstly, I will discuss the motivation.

## Slide 19: Summary
Data visualization of Magnetic field visualization, 2D Magnetic field and Poincare plot of 3D magnetic field perturbations was completed and integrated into virtual tokamak system.
Detailed data processing procedure and visualization steps were specified.
Additional data visualization will be realized and added to the virtual environment.
Experiment data will be fetched from the database and rendered in real-time.