## Slide 1
The views and opinions expressed herein do not necessarily reflect those of the ITER Organization
Daniel Iglesias1, Victor Moncada2, Joris Paret1, Lana Abadie1, Isabel Nunes1, Daniel Sabio3, Sergey Sadakov1, Nathaniel Saura1
1 ITER Organization, 13067 Saint Paul Lez Durance Cedex France
2 CEA-IRFM, 13108 Saint-Paul-Lez-Durance, France
3 Automaticity Solutions SL, 08028 Barcelona, Spain
2nd VOLDA Workshop, November 18–20 2025, Madrid
Data Analysis Strategy for the ITER Tokamak Systems Monitor

## Slide 2: 1. Introduction
PBS.55.GT, Tokamak Systems Monitor uses monitoring algorithms to determine actions and effects at the magnets, VV, blankets, divertor, port plugs, thermal shield and cryostat
These algorithms use the signals of the machine instrumentation as an input for determining the health of the tokamak systems
Main metrics cover forces, peaking factors [1], maximum deformation, heat loads, stress and lifetime effects
[1] Sadakov et al., “Practical Model for the Calculation of Lateral Electromagnetic Loads
in Tokamaks at Asymmetric Vertical Displacement Events (AVDEs)”, Plasma, 2024

## Slide 3: 1. Introduction
TSM needs a tool for Data Analysis both during Operations and for offline detailed studies
The TSM algorithms produce large and heterogeneous amount of data for all tokamak systems
The health state of the machine will be derived from the following variables:
        Reconstruction algorithms values
        Limits and lifetime trends
        Anomaly detection triggers
The operator will need to check and validate the warnings
Early
Warnings

## Slide 4: 2. Monitoring models and data types
Grouped in disciplines [2]:
  Electromagnetic
  Structural
  Thermal* and thermomechanical
  Lifetime
  Anomalies**
[2] Maqueda et al., “Feasibility evaluation and pre-conceptual design of the ITER TSM”, FED, 2023
* See N. Saura – Thermal Surrogate Modeling for the Monitoring of Actively Cooled First Wall Components in ITER
** See J. Paret – Design and Implementation of Machine Learning-Based Anomaly Detection in the ITER Tokamak Systems Monitor
VVGS & TFGS:
Vacuum Vessel and PPs: shells and substructures
Magnets: beams + shells
TKC: shells
Cryostat: beams + shells
Global models Structural
Electromagnetic
40 degree EM model
DFW Thermal

## Slide 5: 2. Monitoring models and data types
Electromagnetic monitoring outputs [3]:
  Vacuum Vessel currents
  Component forces
[3] Villone et al., “Reconstruction of Electromagnetic Loads during Disruptions in ITER”, NucFus, 2025

## Slide 6: 2. Monitoring models and data types
Structural monitoring outputs:
  System/component forces
  Component displacements
Blanket Shield Module
Upper Port Plug

## Slide 7: 2. Monitoring models and data types
Thermal monitoring*:
  Online temperature tracking of relevant points
  Analysis allows calculating the complete thermal maps
Thermomechanical:
  Deformation
  Thermal stress
  Fatigue effects
* See N. Saura – Thermal Surrogate Modeling for the Monitoring of Actively Cooled First Wall Components in ITER

## Slide 8: 2. Monitoring models and data types
ML-based anomaly detection [4]:
  Output of these type of algorithms include flags or spikes in the case of time-dependant anomalies
  Interactivity needed with the plots to link an anomaly to a database (to keep a record), a 3D mesh (to trace it back to a physical location), etc.
  A second use case for the clustering algorithms is under study
Anomaly detection using a neural network on a toy dataset
[4] Paret et al., “ML-based anomaly detection for ITER’s TSM: a gyrotron case study”, TechRxiv, 2025

## Slide 9: 3. HMI high-level specification
TSM POZ currently contains all functionality of TSM for execution and control of the monitoring algorithms
TSM Data Analysis contains the rest, so that it reduces POZ complexity:
  Tokamak health indication
  Early warnings analysis and processing
  Operational data evaluation
  Offline data processing and calibration [5]
Control HMI
Evaluation
Annotations
Data analysis HMI
Status
Offline
[5] Paret et al., “Preliminary machine learning-based calibration strategy for the ITER Tokamak Systems Monitor”, FusEngDes, 2026

## Slide 10: 3. HMI high-level specification
HMI should allow to detect and process all inputs and outputs from TSM, both during plasma operations and offline detail analysis:
  Input sensors:
    Strain gauges ~1000
    Accelerometers ~100s
    Displacement sensors ~10s
    Temperature and flow sensors ~1000
    Electromagnetic diagnostics ~100s
  Output variables:
    Forces and stress ~1000
    Displacements ~100s
    Derived temperatures ~100s
    Heat flux and volume heat maps ~1E6
    Anomalies ~100s

## Slide 11: 4. Architecture
Modular widget-based architecture.
Using technologies unavailable in POZ, hence the need to have a more complete deployment environment.
Linked to a “Events database” to report and label anomalies and other early warnings.

## Slide 12: 4. Architecture

## Slide 13: 5. HMI layouts and workflows
Event detected – Systems state live report [15h34’12”]
Warnings
No warnings
Scarce resources management
Based on lifetime
Based on health limits
and anomalies
Concept definition – Status

## Slide 14: 5. HMI layouts and workflows
Event detected – Systems state live report [15h34’12”]
Warnings
VV under evaluation
Scarce resources management
Based on lifetime
Based on health limits
and anomalies
Concept definition – Status

## Slide 15: 5. HMI layouts and workflows
Event detected – Systems state live report [15h34’12”]
Warnings
VV equatorial port displacement
Scarce resources management
Based on health limits
and anomalies
Based on lifetime
Concept definition – Status

## Slide 16: 5. HMI layouts and workflows
Preliminary implementation – Status

## Slide 17: 5. HMI layouts and workflows
Event detected – Systems state live report [15h34’12”]
System
Magnets
VV
Blanket
Divertor
Cryostat
Thermal Shield
Port plugs
ECH
NB
ICRH
…
Warnings
102 Time 1 Signal A
103 Time 2 Signal B
Warning 102 details
Triggered on time 1
By Signal A in VV : Sector 2
Normal level
Dismiss
Confirm issue
More details
S1 S2 S3 S4 S5 S6 S7 S8 S9
Postpone
Concept definition – Annotation
AI-enhanced summary of the warning

## Slide 18: 5. HMI layouts and workflows
Preliminary implementation – Annotation

## Slide 19: 5. HMI layouts and workflows
Concept definition– Evaluation
Live monitoring of variables
Vacuum vessel sector 2 warning

## Slide 20: 5. HMI layouts and workflows
Preliminary implementation – Evaluation

## Slide 21: 5. HMI layouts and workflows
Preliminary implementation – Offline processing

## Slide 22: 5. Ongoing final design
A thorough comparison was made during 2024 between 3 options:
Developing on top of Paraview
Adapting an existing monitoring tool
Continuing with a dedicated development from scratch
We decided to develop on top of CEA’s ThermaVIP [6], with the following key advantages:
Currently used for operation at WEST, EAST and W7-X,
Known technologies: C++, Qt, etc.
Compatible with ITER UDA,
Open source.
[6] V. Moncada et Al., ”Software platform for imaging diagnostic exploitation
applied to edge plasma physics and real-time PFC monitoring”, FusEngDes, 2023

## Slide 23: 5. Ongoing final design
Current collaboration contract is ongoing, with the following features implemented:
Data archive read and live update through UDA
Fast data streamer subscription and plotting
VTK geometries and data plots allow analysis of 2D and 3D monitoring data
Filtering and representation of monitoring point data

## Slide 24: 6. Conclusions
The ITER Tokamak Systems Monitor data analysis:
Requires treatment of thousands of input and output variables
Will have four main functionalities:
  Health status of the tokamak systems
  Annotations and management of early warnings
  Evaluation of the operational data
  Summaries, offline detail analysis, and calibration of models
Main workflows have been defined
Final design of the data analysis software is well underway

## Slide 25
Thank you
Daniel Iglesias1, Victor Moncada2, Joris Paret1, Lana Abadie1, Isabel Nunes1, Daniel Sabio3, Sergey Sadakov1, Nathaniel Saura1
1 ITER Organization, 13067 Saint Paul Lez Durance Cedex France
2 CEA-IRFM, 13108 Saint-Paul-Lez-Durance, France
3 Automaticity Solutions SL, 08028 Barcelona, Spain
2nd VOLDA Workshop, November 18–20 2025, Madrid
Data Analysis Strategy for the ITER Tokamak Systems Monitor

## Slide 26
References
[1] Sadakov et al., “Practical Model for the Calculation of Lateral Electromagnetic Loads in Tokamaks at Asymmetric Vertical Displacement Events (AVDEs)”, Plasma, 2024
[2] Maqueda et al., “Feasibility evaluation and pre-conceptual design of the ITER TSM”, FED, 2023
[3] Villone et al., “Reconstruction of Electromagnetic Loads during Disruptions in ITER”, NucFus, 2025
[4] Paret et al., “ML-based anomaly detection for ITER’s TSM: a gyrotron case study”, TechRxiv, 2025
[5] Paret et al., “Preliminary machine learning-based calibration strategy for the ITER Tokamak Systems Monitor”, FusEngDes, 2026
[6] V. Moncada et Al., ”Software platform for imaging diagnostic exploitation applied to edge plasma physics and real-time PFC monitoring”, FusEngDes, 2023