## Slide 1
Thermal surrogate modeling for the monitoring of actively cooled first wall components in ITER
N. Saura, J. Paret, D. Iglesias
ITER Organization

## Slide 2
Introduction and motivation
State of the art
  Existing models for continuous monitoring of tokamak first wall are limited to 2D formulations and typically assume limited cooling during the plasma discharge [1]
First wall components characteristics for ITER
  Passively cooled temporary first wall (TFW) for Start of Research Operations (SRO)
  Actively cooled diagnostics first wall (DFW), final blankets FW and divertor
Challenges
  While existing models are valid for TFW, accurate cooling is required for the rest
  3D geometries are relevant for defining the overall thermal state
  Models cannot afford to model the detailed geometry of cooling channels as the number of nodes would increase in numbers of magnitude
Scope of this contribution
  We present herein an evolution of the monitoring models which allow accounting for 3D geometries and cooling effects by combining 2D thermal models with linear interpolations
[1] Fusion Engineering and Design 125 (2017) 71-76

## Slide 3
Defining 2D slices of existing CAD geometry
Surrogate modeling (porous approach) for temperature evolution through MKNIX
Interpolate intermediate plans to approximate the 3D solution
Global overview of the workflow

## Slide 4
I: Surrogate model of the thermal evolution of actively cooled DFW in ITER
  I-A: Surrogate modeling for monitoring
  I-B: Porous Media Approach (PMA) applied for ITER DFW
    Theoretical framework for the PMA
    Validation of the PMA implementation in MKNIX
    Porosity profiles and first results
II: 3D shape and temperature interpolation
  II-A: Signed Distance Function
    Mathematical description
    Example in shape morphing (valid-shape interpolation)
  II-B: Example of interpolation in real geometry: Equatorial Port Plug 12
    Setup of the numerical experiment: thermophysical quantities, orders of magnitude and assumptions
    Global reconstruction from solved planes
    Reconstruction errors for intermediate planes
III: Discussion and Conclusion
Overview of the presentation

## Slide 5
I-A: Incorporating cooling through added porosity
Fine mesh of cooling channels Greedy simulations
Assumptions:
  Radial profiles ();
  Constant thermophysical properties of the coolant;
  Constant velocity and coolant temperature
Cooling channels in the generic DFW
Porous media: energy extraction is modeled as a sink term in the Solid Temperature equation.
Model the added porosity resistance though coolant thermophysical properties

## Slide 6
Add local effect on the solid temperature evolution due to cooling channels [2]
With volumetric heat load and heat flux
Symbols | Quantities
 | Density
 | Specific heat capacity
 | Temperature
 | Thermal conductivity
 | Porosity Resistance
 | Pipe diameter
 | Heat transfer coefficient
 | Pipe effective porosity
Symbols | Quantities
 | Density
 | Specific heat capacity
 | Temperature
 | Thermal conductivity
 | Porosity Resistance
 | Pipe diameter
 | Heat transfer coefficient
 | Pipe effective porosity
Total heat exchange to fluid streams
[2] Nuclear Engineering and Design 421 (2024) 113084
[3] IDM UID 2ABR92 (CFD analysis)
,
Subscript: s solid, l coolant
pipes and in four porosity regions radially defined , ,
Pipeline layout in the generic DFW from
I-B: Theoretical framework for the PMA
(Dittus-Boelter correlation)

## Slide 7
I-B: Validation of the PMA implementation in MKNIX
PMA implementation in local FEM solver: MKNIX
Take a simple case where analytical solution is known (differential equation)
Linear interpolation between porosity regions (simple case)
Time (s)

## Slide 8
Model the cooling effect by a gaussian which full width half maximum (FWMH) is the pipe radius
Porosity profile: sum of the gaussians picked at the pipes center
I-B: Porosity profiles and first results

## Slide 9
I-B: Porosity profiles and first results
We model the cooling effect by a gaussian which full width half maximum (FWMH) is the pipe radius
Satisfy the temperature constrain from CFD (Overestimation )
Similar temperature in cooling pipes domain
Require few seconds of computation
Current implementation of hydraulics effects varies with only
Reference results (CFD)
MKNIX-Porosity results (FEM/Surrogate)

## Slide 10
II-A: Signed Distance Function - Mathematical description
Signed Distance Function (SDF) gives the distance to a boundary of a given a rasterized domain (mask,
Let and at and two domains, masks and SDFs.
Any intermediate shape domain at can be obtained interpolating the SDFs
  and

## Slide 11
II-A: Example in shape morphing (valid-shape interpolation)
: smooth transition
Interpolate “valid” region used for temperature interpolation
General to any shape
α
Evolving masks/shapes
Reference planes/masks

## Slide 12
II-B: Setup of the numerical experiment
Z coordinates (SALOME)
Z coordinates (SALOME)
~Fine mesh to account for high fluid velocity (see after)

## Slide 13
II-B: Setup of the numerical experiment: thermophysical quantities, orders of magnitude and assumptions
Highly turbulent flow: and flow mean constant velocity:
Mean and constant fluid temperature
Heat transfer coefficient
We use the same cooling channels layout as the generic one artificial hot spots

## Slide 14
Cooling channels layout comparison
Velocity contour in first layer of cooling channels for generic DFW
Velocity contour in first layer of cooling channels for EPP12 DFW (bottom)
II-B: Setup of the numerical experiment: thermophysical quantities, orders of magnitude and assumptions

## Slide 15
II-B: Global reconstruction from solved planes
First step:
Solve with MKNIX and
Interpolate nodal temperature (matplotlib.Tri)
Compute SDF for each solution at
Compute for any between and and
Infer and
Where only intersects (idem ) (it avoids NaN + any real = NaN)
At high velocity: requires ~20 seconds for all the slices (parallelizable)
Then
Takes ~ 2 seconds to compute 118 intermediate () solutions

## Slide 16
II-B: Global reconstruction from solved planes
Reconstructed 3D (TSM) few seconds in total
Reference results (CFD), computation time not specified (usually >> TSM)
~
~

## Slide 17
II-B: Reconstruction errors for intermediate planes
Z coordinates (SALOME)
Z coordinates (SALOME)
Shape and temperature are well interpolated
Assuming similar heat load in the poloidal direction

## Slide 18
II-B: Reconstruction errors for intermediate planes
Z coordinates (SALOME)
Z coordinates (SALOME)
Errors in the reconstruction of both shape and temperature
Interpolation is purely vertical: it expects that cooled domains remain the same
Modeling errors on the rightmost edge of the PP opening Needed to add heat diffusivity to DSM

## Slide 19
II-B: Reconstruction errors for intermediate planes
Comes from the previous reference solution (wider exposed section)
Sharp variation of the shape
Error coming from next reference solution is corrupting the temperature reconstruction

## Slide 20
III: Discussion (PMA)
The PMA allows several tunable parameters (scenario exploration):
Regarding the cooling:
  Fluid velocity and temperature
  Regime flow
  Thermophysical properties
Regarding the geometry:
  Number of pipes, positions, diameter
  Vertical pitch between pipe layers to control the effective porosity
  Tunable Gaussians FWHM in the porosity profile
The main limitations:
  Radial variations of porosity only (MKNIX)
  Constant heat load on the geometries (MKNIX)
  Constant velocity, temperature and thermophysical quantities for the modelled fluid (one way coupled)
  High velocity requires finer meshes
Results are still promising BUT limitations appear along with geometry complexity
Simulations are fast, cheaper and completely independent (one plan to another)
Flexible under the current constraints

## Slide 21
III: Discussion (2D 3D interpolation)
Current implementation shows promising results
  Fast 3D interpolations from reference plans
  Flat region are perfectly interpolated
  Global structure looks good but requires off-line selection of the reference planes
Improvements will be to induce global geometry awareness in the blending process to improve the plasma front temperature interpolation

## Slide 22
Conclusion
Current pipeline to develop fast surrogate models for the monitoring of actively cooled components of ITER DFWs based on Porous Medium Approach and 2D 3D interpolation
PMA implementation in our local solver MKNIX has been validated and first encouraging results have been obtained for simple and complex geometry
The interpolation part has also showed interesting results/possibilities.
Improvements required on the implementation aspects (1D porosity 2D etc.)
Interpolation strategy may have to be thought again especially close to varying geometry
Fast 3D model: from ~5 to 30 seconds for a complex 3D geometry depending on

## Slide 23
Nathaniel Saura
Second Visualizing Offline and Live Data with AI (VOLDA) Workshop
Thank you!

## Slide 24
I-B: Incorporating cooling through added porosity
In the Solid temperature equation, we add the local effect due to the fluid in the cooling channels [1]
Symbols | Quantities
 | Density
 | Specific heat capacity
 | Temperature
 | Solid thermal conductivity
 | Porosity Resistance
 | Pipe diameter
 | Heat transfer coefficient
 | Pipe effective porosity
 | Mean fluid velocity
 | Dynamic and kinematic viscosity
Symbols | Quantities
 | Density
 | Specific heat capacity
 | Temperature
 | Solid thermal conductivity
 | Porosity Resistance
 | Pipe diameter
 | Heat transfer coefficient
 | Pipe effective porosity
 | Mean fluid velocity
 | Dynamic and kinematic viscosity
Represents the total heat exchange to fluid streams
[1] Nuclear Engineering and Design 421 (2024) 113084
[2] IDM UID 2ABR92 (CFD analysis)
,
For Turbulent regime ( and), Dittus-Boelter correlation, with exponent from [1]
Where and
Subscript: s solid, l coolant
Coolant thermophysical quantities supposed constant
Porosity varies radially according to number of pipes and their diameters

## Slide 25
I-B: Incorporating cooling through added porosity
Add local effect on the solid temperature evolution due to cooling channels [2]
Symbols | Quantities
 | Density
 | Specific heat capacity
 | Temperature
 | Thermal conductivity
 | Porosity Resistance
 | Pipe diameter
 | Heat transfer coefficient
 | Pipe effective porosity
Symbols | Quantities
 | Density
 | Specific heat capacity
 | Temperature
 | Thermal conductivity
 | Porosity Resistance
 | Pipe diameter
 | Heat transfer coefficient
 | Pipe effective porosity
Total heat exchange to fluid streams
[2] Nuclear Engineering and Design 421 (2024) 113084
[3] IDM UID 2ABR92 (CFD analysis)
,
Subscript: s solid, l coolant
pipes and in four porosity regions
, ,

## Slide 26
Interpolation
domain
extrapolation
domain

## Slide 28
I-B: Incorporating cooling through added porosity
Cooling channels in the generic DFW
Fine mesh of cooling channels Greedy simulations
Porous media: energy extraction is modeled as a sink term in the enthalpy equation.
Model the added porosity resistance though coolant thermophysical properties
Assumptions:
  radial profiles
  constant properties
  gaussian profiles around center of pipes